Company Standard SТО № 9.07-П01

Supplier Process Audit for Compliance with Requirements of GAZ Group

Version 4.0

Nizhny Novgorod 2017

Contents

1. Purpose and scope	3

2. Terms, definitions and reference documents	3

3. Essential elements	4

4. Implementation procedure	8

5. Changes	12

6. List of appendices										  13

# 1. Purpose and scope

1.1 Main purposes

1.1.1 The purpose of this Standard is to regulate the evaluation of external suppliers for compliance with GAZ Group requirements.

1.1.2 In terms of its substance, this Standard relies on the requirements of the following standards: ISO 9001:2015, IATF 16949:2016, VDA 2, VDA 6.1, VDA 6.3 and SТО 9.07-МУ01 and is aimed at helping GAZ Group to achieve its supplier quality assurance objectives.

1.1.3 Evaluation of suppliers’ processes for compliance with GAZ Group requirements pursues the following objectives:

- understand how competent suppliers are and what supplier-related risks can be expected;

- determine areas for possible improvement and gradually streamline the requirements  to suppliers.

1.2 Scope

This Standard is binding on all companies which are part of GAZ Group. The procedures laid out herein apply only to external suppliers of piece materials, semi-finished parts and components (goods) that are expected to be used in the production of GAZ companies’ core products and do not cover goods supplied by existing suppliers for existing projects (except when a supplier audit is requested by the procurement, quality, asset protection or economic security departments) as well as parts supplied by one GAZ company to another.

The implementation procedure is described in Section 4.

1.3. Risks and performance indicators

1.3.1 The main risks associated with this process are:

- biased evaluation;

- failure to perform evaluation due to the lack of resources.

1.3.2 Key performance indicators will be deemed to have been achieved if:

- the supplier audit plan was met;

- competencies and skills of suppliers are known well enough to inform the choice of suppliers and/or allocation of volumes among suppliers.

1.3.3 The achievement of key performance indicators will be tracked:

- through their inclusion in the KPIs of supplier quality assurance managers;

- during meetings of the Nomination/Tender Committee

# 2. Terms, definitions and reference documents

2.1. Abbreviations:

IATF- International Automotive Task Force

KPI- Key Performance Indicators

SQA&D – Supplier Quality Assurance and Development Department

APQP- Advanced Product Quality Planning

PPAP- Production Part Approval Process

FMEA- Failure Modes and Effect Analysis

dFMEA- Design Failure Modes and Effect Analysis

pFMEA- Process Failure Modes and Effect Analysis

MSA- Measurement System Analysis

S- seriousness (measurement of how serious the effect of the failure is (ranging from 1 to 10)

О- occurrence (measurement of how frequent the failure is (ranging from 1 to 10)

CS-controlled shipping

SPC- Statistical Process Control

Cp, Cpk – measure of process capability

Cm, Cmk – measure of equipment capability

ТРМ- Total Productive Maintenance

Poka-Yoke – fail safe device/operating principle

EAQF – French Automotive Quality Standard

AVSQ – Italian Automotive Quality Standard

DVP- Design Verification Plan

SOP- start of production

5S – workplace organization method

8D- eight discipline (problem resolution method consisting of 8 steps)

GAZ– any company that is part of GAZ Group

PD – procurement department;

SQA- Supplier Quality Assurance

PS – Production System

QMS- Quality Management System

SPM– Scheduled Preventive Maintenance

RAP – remedial action plan

IPE – individual protective equipment

2.2 Applicable regulations

GOST R ISP9001-2015 Quality Management Systems. Requirements.

IATF 16949:2016 Quality Management System Requirements for Automotive Production and Relevant Service Parts Organizations.

VDA 2 Supplier Quality Assurance

VDA 6.1 Quality Management in the Automotive Industry. Serial Production.

VDA 6.3 Quality Management in the Automotive Industry. Process Audit.

SТО 9.07-МУ01 Requirements to suppliers of GAZ Group.

SТО №9.01–П.09 Organization of tenders for selecting suppliers of new parts for product projects.

SТО №9.01-П13 Organization of tenders by the procurement department of GAZ Group Management Company.

# 3. Essential elements

3.1. Inputs and end products of the supplier evaluation processes

3.1.1. Inputs:

- audit plan;

- supplier audit request/order;

- resources (human, financial, etc.);

- codified requirements to GAZ Group suppliers (SТО 9.07-МУ01).

3.1.2. End products:

- findings of supplier audit for compliance with GAZ Group requirements;

- identified areas/potential for improvement.

3.2. Guiding principles:

- openness – evaluation criteria and results are publically known;

- equality – same terms, criteria and methods of evaluation apply to all suppliers;

- economy – evaluation may be conducted by respective specialists of any GAZ company while its results will  be recognized by all other GAZ companies.

3.3.  Applicability:

3.3.1. An audit must be conducted with respect to any external supplier who does not have an IATF 16949:2016 conformity certificate issued by an IATF-approved certification agency for a specific product. Head of SQA may make an informed decision to order an audit of a supplier who has such conformity certificate.

3.3.2. Until the SQA service has completed the audit, the supplier requires temporary approval in accordance with the provisions of SТО №9.01–П.09.

Audit requests sent by the Procurement Dep. to the SQA Dep. shall contain the objective of the audit, the name and location of the supplier, name of the product, contact person and an Audit Form.

3.3.3. Processes rated as “red” may be re-audited by the SQA Dep. only if specifically requested by the Procurement Dep. and if there is an official notice that earlier irregularities and inconsistencies have been corrected.

3.4.  Minimum qualifications required from personnel engaged in evaluating suppliers’ compliance with GAZ Group requirements:

- higher education in engineering;

- at least 3-year experience in the automotive industry;

- experience with APQP methods and tools and knowledge of the requirements GAZ Group set to external suppliers;

- basic knowledge of IATF 16949 and РРАР, FMEA, MSA, SPC, VDA 6.3, and ISO 9001:2015.

- participation in not fewer than 3 supplier evaluations as an apprentice

3.5. Supplier audit planning:

3.5.1. Supplier audits are conducted on the basis of:

- quarterly audit schedules (Appendix 1);

- urgent request of the Procurement Dep.;

- direct orders given by procurement director/Procurement Committee

3.5.2. Suppler audit schedules are prepared basing on:

- requests from Procurement Dep. and other units;

- notices by which suppliers inform GAZ that irregularities identified in the course of the previous audit have been corrected and that they are prepared for the second audit;

- information with regard to the quality of current supplies.

3.5.3. Supplier audit schedules are made quarterly for each GAZ company. These schedules may be changed or modified in the current quarter basing on a decision of the SQA director, approval of the procurement director is not required.

3.5.4.  The schedule implementation report must show how many processes were audited (each suppler may have more than one process/product that must be audited).

3.6. Supplier process audit principles:

3.6.1. Audits are based on collecting and analyzing objective evidence characterizing the suppliers’ technical capabilities and quality management system and their compliance with the criteria laid out in the Supplier Process Audit Card (Appendix 2). Compliance with each criterion will be measured by awarding points where 0 is the lowest and 3 is the highest:

- «0»– risk of late shipments or substandard products is high;

- «1»– high to moderate risk;

- «2»– moderate to little risk;

- «3»– little or no risk.

3.6.2. Supplier processes are audited in relation to a specific manufacturing technology and (or) manufacturing of a specific product (product type).

3.6.3. In case a criterion is irrelevant to the supplier’s operation or inapplicable to the manufacturing process being audited, respective box must be marked as N/A (not applicable).

Criteria that for one reason or another (the reason must be clearly stated in the Supplier Process Audit Card) were not addressed in the course of the audit must be marked as U/N (unaudited).

N/A and U/A marks are not taken into account when calculating the final score.

3.6.4.  Whenever fewer than 3 points were awarded, the Supplier Process Audit Card must provide respective comments.

3.6.5. Data in the Supplier Process Audit Card is used as a basis for filling out the Supplier Process Audit Report (Appendix 3) which must contain the final evaluation result:

- GREEN (more than 80 points)- supplier’s quality assurance capabilities were confirmed; Cooperation is recommendable; little or no risk.

- YELLOW (60 to 80 points) - quality assurance capabilities are contingent on making and implementing a remedial action plan (Appendix 4); a follow-up audit is necessary; low to high risk.

- RED (less than 60 points)- supplier’s quality assurance capabilities were not confirmed; high risk. This means that:

- the supplier cannot be used as a source of parts/materials for the new product;

- with respect to existing supplies the Procurement Dep. must take any of the 3 courses of action below:

а) use a replacement supplier(s) that has proper evaluation score;

b) de-monopolize the supplier; respective action plan is subject to approval of the procurement director/head of the Nomination Committee;

c) work toward raising the quality of supplier’s processes to an acceptable level. The feasibility of this course of action must be confirmed by SQA and PS while respective decision requires approval of the procurement director.

3.6.6. A process will be in the red zone regardless of the final score if the supplier does not have the equipment necessary for fulfilling the order (section № 5.1.4 of the Supplier Process Audit Card).

3.6.7.  Products of processes that fall into the red zone may be nominated only subject to express consent of the chairperson of the Tender Committee.

3.6.8. If any of the items marked with (*) received 0 or 1, the entire process may not be rated higher than YELLOW regardless of the final score.

3.6.9. Audit results are cancelled or a new audit is conducted whenever:

- no effective steps have been taken to improve the quality of supplied parts/materials;

- shipments have been repeatedly delayed because of technical issues;

- follow-up on-site audits found that supplier’s manufacturing processes were unsatisfactory;

- there is new negative information about the supplier;

- the supplier did not supply anything to any GAZ company for more than a year.

- the supplier did not produce any product for any GAZ company for more than 6 months.

3.7. Audit of suppliers that have no production facilities of their own:

3.7.1. Suppliers that supply or have an intention to supply products produced at facilities operated by parties other than the supplier (e.g. trade houses, dealers, logistic operators, etc. (collectively referred to as “intermediaries”)) may be audited in exceptional cases.

Intermediaries may be audited at the discretion of the procurement director/chairman of the Tender Committee. The following must be taken into account:

А) if an on-site visit to the manufacture is impossible, purchasing experts shall conduct an audit and fill out the Supplier Audit Check-List as required by SТО №  9.01 –П.09. The intermediary must be able to operate Dialog GAZ system (with respect to defects);

B) if it is possible to visit both the intermediary and the manufacturer, SQA experts shall conduct an audit and fill out a single Supplier Process Audit Card.

3.8. Approval of audit results:

3.8.1. SQA&D shall appoint a process administrator to manage supplier audit procedures throughout GAZ Group in a centralized way.

3.8.2.  The administrator will have the following responsibilities:

- prepare quarterly supplier process audit schedules and post them, once they are  approved, at GAZ Group’s web site;

- arrange and coordinate the supplier process audit work, which includes preparing and sending requests to suppliers, notifying them of the objectives and dates of the visits, monitoring the compliance with the audit schedule and making changes to it whenever necessary, making sure that auditors submitted property filled-out audit cards and reports in a timely manner, etc.;

- prepare final supplier process audit reports and submit them to the head of SQA for approval;

- make the audit results known to the suppliers;

- maintain a list of audited supplier processes (Appendix 5) and post it at GAZ Group’s web site;

- keep all documents relating to supplier process audits, including copies of remedial action plans and respective implementation reports received from suppliers.

3.8.3.  Supplier process audit results and reports are subject to approval of the head of SQA in each respective GAZ company (Division).

3.8.4. GAZ companies (Divisions) shall send supplier process audit results and reports to the process administrator in GAZ Group MC to make this information available to other GAZ companies (Divisions).

3.8.5. Supplier process audit results will be used for the purposes of conducting procurement procedures in accordance with SТО №9.01–П.09, SТО №9.01-П13, and other regulations in effect in GAZ Group.

3.9. Confidentiality:

When conducting supplier process audits every person involved in this work shall keep the information they received in the course of the audits confidential (no disclosure to third parties) as required by respective regulations in effect in GAZ Group.

# 4. Implementation procedure

| № | Action | Action owner | Timeline | Input documents | Description | Output documents |
| --- | --- | --- | --- | --- | --- | --- |
| 1 | 2 | 3 | 4 | 5 | 6 | 7 |
| 1 | Appoint a procedure administrator in GAZ Group MC | GAZ Group procurement director | When necessary | Draft appointment order | A procedure administrator is appointed by GAZ Group procurement director’s order and remains in that capacity until replaced by another appointee. | Appointment order |
| 2 | Assess the need of auditing supplier processes | Procurement departments and other units (development dep., quality dep.) | When necessary | Check-list showing the results of the initial visit to supplier’s facilities Procurement committee meeting minutes | Whenever there is a need to audit supplier processes, respective request will be sent to the head of SQA The request must state the time period/date when the audit needs to be conducted. The audit request must be served not later than 15 business days before the scheduled date of the nomination or tender. | Written supplier process audit request |
| 3 | Make a list of supplier processes that have to be audited | Procedure administrator | Two weeks before the start of the following quarter | Written audit request RAP implementation notice from suppliers Current supplies quality data | A list of suppler processes auditable in the following quarter is drafted and submitted for approval to SQA&D director. The draft list may be changed or modified, if necessary. If supplier processes must be audited in the current quarter and the supplier is ready for the SQA team’s visit, that supplier will be added to the audit schedule for the current quarter (see Item 6). | Approved list of auditable supplier processes |
| 4 | Make and obtain approval for a supplier process audit schedule | Procedure administrator | 2 business days after approval of the list of supplier processes that have to be audited | Approved list of supplier processes that must be audited | All supplier processes on the list will be assigned time slots basing on their urgency and/or suppliers’ capabilities. Once completed, a draft audit schedule will be signed off by SQA&D director and submitted to GAZ Group procurement director The schedule requires approval of GAZ Group procurement director. | Order approving the quarterly supplier process audit schedule |
| 5 | Coordinate the audit time with the supplier | Procedure administrator (with the help of the procurement expert who initiated the audit) Experts of GAZ companies | Not later than 1 week before the estimated date of the visit | Approved supplier/process audit schedule Written supplier process audit request | The supplier will be served a written request saying when the visit will presumably take place. The request is accompanied by a blank Supplier Process Audit Card. If supplier process audits are conducted by SQA teams based in GAZ locations other than Nizhny Novgorod, those GAZ companies will be responsible for negotiating visits with suppliers. | Written request sent to the supplier |
| 6 | Change/modify the supplier process audit schedule | Procedure administrator | Within 3 business days after receiving supplier’s answer | Written audit request Response letter from supplier RAP implementation notice from supplier | The audit schedules will be changed/modified when necessary and if a compromise was achieved among SQA, procurement dep., and supplier’s management. Changes/modifications to the current audit schedule will be made at the discretion of the head of SQA, approval of the procurement director is not required. | Modified audit schedule for the current quarter |
| 7 | Conduct suppler process audit | SQA team | As scheduled | Audit schedule Filled-out initial visit check list Product quality information | The process audit must be preceded by a meeting with supplier’s management to brief them on the objectives, scope and the evaluation criteria, reach an agreement on the rules and procedures to be followed during SQA team’s presence at the plant site, agree whether it is possible to take photo/video and outline possible outcome depending on the audit results. In the course of the audit, supplier processes will be checked for compliance with the evaluation criteria listed in the Audit Card and rated accordingly by awarding points. The awarding of points must be supported by factual observations and/or documentary evidence. The Supplier Process Audit Card must state what exactly is audited- manufacturing technology, product or both. If fewer than 3 points are awarded, the Card must explain why. The audit must be followed by a meeting with supplier’s management to brief them on the preliminary findings and conclusions of the audit and whether a RAP might be necessary. Completed Supplier Process Audit Cards must be submitted to the procedure administrator not later than 3 business days after the SQA team came back from the audit. | Audit Card Summary report |
|  |  |  |  |  | In addition, there must be a summary report containing the conclusions and proposals with respect to supplier’s manufacturing facilities (preferably with photos). The intended recipient of this report is the Tender Committee to which it is presented upon request. The summary report requires prior approval of the head of SQA. |  |
| 8 | Approve the audit results | Head of SQA | Within 2 business days after making the audit report | Audit report Summary report Audit card (if necessary) | The procedure administrator will submit the Audit Report to the head of SQA for approval. The report must be accompanied by all audit materials. | Approved audit report |
| 9 | Bring the audit result to supplier’s notice | Process administrator | Within 2 business days after the report was approved | Approved audit report | The procedure administrator will serve audit result notices to the supplier and procurement/SQA dep. In case any processes fall into RED or YELLOW zone, respective RAP will be requested. The audit results will be added to a database on GAZ Group’s web site. | Audit result notice. Suppler Process Audit Card |
| 10 | Carry out remedial actions | Supplier (SQA/procurement expert) | According to supplier’s internal procedures | Supplier Process Audit Card | After receiving the filled-out Audit Card the supplier has 10 days to present a RAP. A copy of the RAP must be sent to the procedure administrator. Once the RAP implementation deadline has passed, the supplier must present respective notification/report | RAP RAP implementation notice |

# 5. Changes

| Version | Date and instrument of approval | Effective date | Approved by |
| --- | --- | --- | --- |
| 04 | Order № 89/001 dated 24.04.2018 | 11.05.2018 | GAZ Group President V. Sorokin |
| 04 | Order № 110/001 dated 29.04.2022 | 25.05.2022 | GAZ Group President V. Sorokin |

6. Appendices

| Appendix 1 | Quarterly Supplier Process Audit Schedule |  |
| --- | --- | --- |
| Appendix 2 | Supplier Process Audit Card |  |
| Appendix 3 | Supplier Process Audit |  |
| Appendix 4 | Remedial Action Plan |  |
| Appendix 5 | List of suppliers found compliant with GAZ Group requirements |  |

# Text boxes

Приложение к Приказу от 04.07.2017 № 132